## Slide 1
Design and Performance Analysis of Solar PV system using PV-syst
A
It shines on us too and helps us all grow.

## Slide 2: CONTENT
Introduction
Steps in analysis
Types of Losses
Results
conclusion
references

## Slide 3: INTRODUCTION
What is PV-syst Software
One of the oldest software, developed by University of Geneva.
Main features:
  Meteorological data analysis
  Complete database of PV Module, Inverter, & Meteo data.
  Import of solar radiation data from SolarGIS, Meteonorm, NASA-SSE and many more.
  Also import files as .PAN files, .OND files, ,BAT files.
  Shadow analysis using 3D models.
  Design simulation of Grid connected, Standalone system.
  Economic Evaluation.

## Slide 4: Steps in analysis
Location (geographical detail)
  Coordinates: Latitude & Longitude
  Address: Department of Sustainable Energy Engineering.
Import Meteo data
  Used Meteonorm data for analysis from
Location
Import Meteo data
Orientation
System design
Selection of PV module & Inverter
Shading Analysis
Module Quality loss/Mismatch loss/Soiling loss
Simulation execution

## Slide 5: Steps in analysis

## Slide 6: Steps in analysis
In orientation part the field parameters includes azimuth angle, tilt angle.
Quick optimization tools:
  Yearly irradiance yield
  Summer (Apr- Sep)
  Winter (Oct-Mar)
Orientation

## Slide 7
Department of Sustainable Energy Engineering
System design

## Slide 8: Steps in analysis
Selection of PV module & Inverter

## Slide 9
Steps in analysis
Shading Analysis
Near Shading
  Shading caused by objects that are close to the solar panel array, such as buildings, trees, or other objects.
  Significant impact on the performance of a PV system.
  It create "hot spots" on the solar panels and reduce the overall efficiency of the panel.

## Slide 11: Types of Losses
Temperature Losses
  With the increase in temperature of PV module the efficiency decreases.
Reflection losses
  Occur when sunlight reflects off the surface of a PV panel.
Wiring losses
  The electrical wiring and connections cause losses due to resistance, which can reduce the overall efficiency of the system.
Mismatch losses
  Mismatch losses occur when different PV panels in an array have different electrical characteristics
Ohmic/Resistive Losses
  Occur when electrical current flows through the internal resistance of the panel's cells and interconnections (metal contacts and busbars used to interconnect the cells).

## Slide 12: results
The normalized productions of each month has been stated, It gives the three important parameters:
  Collection loss (PV-array losses):- Refers to the energy lost in the PV module itself :-
  System Loss:- Refers to the energy lost in the various components of the PV system outside of the PV module, such as the wiring, inverters, and transformers :-
  Produced useful energy (Inverter output):-

## Slide 13: results
The performance ratio of each month has been stated.
It is a measure of the efficiency of a PV system.
Optimal Range
Obtained Value of

## Slide 14: results
global horizontal irradiation, horizontal diffuse irradiation, ambient temperature, and global incident radiation. performance ratio, energy injected into Grid, effective energy at the output of the array

## Slide 15: results
Loss diagram shows all the losses that occur in the system step by step.
is falling in this region to the PV system.
Due to IAM losses and soiling losses the total energy generated in this system is where the efficiency is at STC.
Finally, and the rest of energy is lost due to mismatch loss, inverter loss during operation and Ohmic loss.

## Slide 16: results
Finally, and the rest of energy is lost due to mismatch loss, inverter loss during operation and Ohmic loss.

## Slide 17: conclusion
Design and performance analysis of grid-connected PV system in Department of Sustainable Energy Engineering at IIT Kanpur.
The system production is and the specific output is , the performance ratio is , and the system losses is .
The software PV-syst examines any kind of losses.

## Slide 18: conclusion

## Slide 19: references
https://www.google.com/intl/en_in/earth/
https://www.pvsyst.com/help/index.html?contents_table.htm
https://www.sciencedirect.com/science/article/pii/S2214785321058259?via%3Dihub